## GUARANTEED SPECIFICATION OF RUSSIAN DIESEL GAS OIL D2 GOST 305-82

## SPECIFICATION -“RUSSIA GAS OIL (D2)”

| RUSSIAN D2 GAS OIL L0.2 -62, GOST 305-82 |
| --- |
| Component | Unit | Min. | Max. |
| Density@ 20 deg C | Kg/m3 | 0 | 0,870 |
| Colour |  |  | 2,0 |
| Flash point, PMCC | deg C ( ºC ) | 57 | 62 |
| Kinematic viscosity @20 deg C | CST | 3,0 | 6,0 |
| Pour point | deg C ( ºC ) | (*) | -10,0 |
| Cloud point | deg C ( ºC ) | (*) | -5,0 |
| Mercaptan sulphur |  |  | 0,004 |
| Acidity, mg / 1000 cm3 |  |  | 5 |
| Iodine number | g/100g |  | 6 |
| Ash | %wt |  | 0,01 |
| Total Sulphur | %wt | 0,005 | 0,02 |
| Copper corrosion | 3hours@ 50 deg C | (typical) | 1 A |
| CCR on 10% Residues | %wt |  | 0.20 |
| Cetane index |  | 45 |  |
| Distillation range: |  |  |  |
| - 50% Recovered Volume | deg C ( ºC ) |  | 280 |
| - 90% Recovered Volume | deg C ( ºC ) |  | 360 |
| - Bacteria MBC | Fibred / it |  | 500 |
| - Bacteria CFU | Fibred / it |  | 1000 |

(*) 	Summer from March to October		     (PP - 5.0 degrees C)

Summer from March to October		     (CP - 0.0 degrees C)

Winter from November to February		     (PP - 10.0 degrees C)

Winter from November to February		     (CP – 5.0 degrees C)	The product is guaranteed by Seller not to contain bacteria and other living organism contamination above normal level (1,000 CFU/I).