## SPECIFICATION OF RUSSIAN AVIATION KEROSENE COLONIAL GRADE 54 JET FUEL (JP54)

| PROPERTY | UNIT | RESULT | TEST-IP | METHOD | ASTM |
| --- | --- | --- | --- | --- | --- |
| ADDITIVES Antioxidant in hydro processed fuel Antioxidant non hydro processed fuel Static dissipater first doping ASA-3 Stadis 450 | mg/I mg/I mg/I mg/I | min/max min min min | 17/24 24 1 3 |  |  |
| COMBUSTION PROPERTIES Specific energy, net Smoke point Luminomitter number Naphthalene’s | mJ/kg mm % vol | min min min max | 18.4 19 45 3 |  | D4808 D1322 D1740 D1840 |
| COMPOSITION Total Acidity Aromatics Sulphur, Total Sulphur, Mercaptan Doctor, test | mg KOH/g % vol %mass %mass | max max max max | 0.01 22 0.30 0.003 | 354 158 107 342 30 | D3242 D1318 D1266/2 D3227 D4952 |
| VOLATILITY Initial Boiling Point 10% vol at C 20% vol at C 50% vol at C 80% vol at C End point Recovered residuals Loss Flash Point Density at 15 C | Centigrade Centigrade % vol % vol Centigrade kg/m2 | max max max max max min/max | Report 240 Report Report Report 300 1.5 1.5 42 776/840 | 123 170/303 180/385 | D96 D56/382 D1298 |
| LOW TEMPERATURE Freezing Point | Centigrade | max | -40 | 15 | D2256 |
| CORROSION Corrosion, copper (2hrs at 100C) Corrosion, silver (4hrs at 50C) |  | max max | 1 1 | 154 227 | D130 |
| STABILITY Thermal stability control, Temp. 280C Filter pressure, differential Tube deposit rating (visual) | mm/Hg | max max | 323 25 | <3 |  |
| CONTAMINATIONS Existent Gum Water reaction, interface rating Fuel with static dissipater additives Fuel without static dissipater additive | mg/100ml | max max min min | 7 16 75 85 | 131 258 | D361 D1084 D3648 |
| CONDUCTIVITY Electrical conductivity | p3/m |  | Report |  |  |